Wireless Control Chain Actuator with Adjustable Stroke

Installing Instruction

| Package List |  |
| --- | --- |
|  | Description | Q’ty |  |
| a | Chain Actuator | 1 |  |
| b | Mounting Bracket | 2 |  |
| c | Hex Head Screw | 2 |  |
| d | Connector | 1 |  |
| e | Latch | 1 |  |
| f | φ5 Self-tapping Screw | 8 |  |

Dimension and Wiring Diagram

Parameters

|  | Unit | Specification |
| --- | --- | --- |
|  |  | CH - DC24V | CH - AC220V |
| Force | N | 250 | 250 |
| Max Current | A | 0.6 | 0.15 |
| Stroke | mm | 150-200-250-300 | 150-200-250-300 |
| Speed | mm/sec | ~10 | ~10 |
| Operating Voltage | V | DC24V±10% | AC220V±10% |
| Temps | ℃ | -20~ +75 | -20~ +75 |
| IP Class | IP | 32 | 32 |

- Applications: top/bottom/side hinged windows, pivoted windows, inward/outward opening windows, skylights…

- Different brackets offered；

- Chain options: carbon steel or stainless steel；

- Stroke, force and finish color can be customized；

- MCU inside

- Electronic overload cutoff.

Installation Steps:

- Find the point to fix the connector, horizontally it must be in the middle of window frame; vertically it need to be in a proper position which can make the chain and casing move freely and not scratched or blocked by the window frame, as picture 1；

- Fix the connector with 2 pcsφ5*25mm self-tapping screws, as picture 2；

- Find the positions for mounting brackets according to the position of connector.  The chain need to come in/out vertically to housing of actuator. Fix each mounting bracket with 3 pcsφ5*25mm self-tapping screws , as picture 3；

- Put the actuator between the 2 mounting brackets, fix it with 1 pc hex head screw on each side. Insert the latch into the connector and head of chain, screw it tightly, as picture 4.

- There are 2 different ways to fix the mounting brackets, depending on whether there is window sill. As picture 5 & 6.

Remote Setting:

- Get the power connected;

- Switch remote to the channel that you want to set;

- Click the remote setting button in the actuator, then indicator on actuator flashes one time;

- Press any key of  OPEN/STOP/CLOSE for more than 1.5 seconds, then indicator flashes 4 times, setting finished.

Deleting memory: press remote setting button for 10 seconds, then indicator flashes 3 times, all memories deleted.

Applications

Safety Note:

- Test the actuator at least one working cycle to make sure it works well before the installation.

- Before installation make sure the stroke of actuator is smaller than max opening range of the window sash.

- The housing and chain can not be scratched or blocked by the window frame, they need to be at least 3mm away from the window frame. .

- Make sure the power is disconnected before installation.

- Do not put your hands between window sash and frame when the actuator is working.

- Trained professional staff only for the installation.

- Indoor use only.

- Before installation, find out the input voltage of the actuator is DC24V or AC220V .

- Before installation, make sure the window is working well.

- Regularly check the aging condition of wire and fasten screws, at least one time a year.

- Please do not rotate the stroke control switch when the power is connected.